## Slide 1
Principle of Communications
--- The Wireless Channel
Speaker Teacher：Dr. Xiang Cheng
（程 翔）
Research Center of Wireless Communications and Signal Processing
Institute of Modern Communications
School of Electronics Engineering and Computing Sciences

## Slide 2: Teaching Contents
Why Study Wireless Channels?
What Are Wireless Channels?
Three Phenomena in Wireless Channels
Multipath Fading
Summary

## Slide 3: I. Why Study Wireless Channels?
Any wireless communication system basically includes three parts:
Tx and Rx can be designed to make the system present better tradeoff between reliability and efficiency.
Wireless channels cannot be engineered!
System
Design
Transmitter
(Tx)
Wireless
Channel
Receiver
(Rx)
The concept of tradeoff appears ubiquitously in the investigation of wireless communications！
Enabling foundation for successful analysis and design of any wireless system!
Knowledge of Wireless Channels

## Slide 4: II. What Are Wireless Channels?
Base station
Shadowing
（阴影效应）
Scattering（散射）
Diffraction
（衍射）
Line-of-sight path {LOS}
Scattering
（散射）
Mobile station
Reflection（反射）
Wireless channels are the real environments in which the Tx and Rx are operating.

## Slide 5: Common Problems
Fail to see the forest for the trees.
Draw a trolley without raising head to look the road.
Path Loss
Shadowing
Small Scale Fading
Channel Impulse Response
Frequency Selectivity
Time Selectivity
Space Selectivity
Delay dispersion
Doppler Dispersion
Angle Dispersion
Coherent Time
Narrowband Channel
Wideband Channel
Coherent Bandwidth
Fast Fading Channel
Delay Spread
Slow Fading Channel
Provide a unified and conceptually simple explanation of a morass of concepts for wireless channels！

## Slide 6: III. Three Phenomena in Wireless Channels
Base station
Shadowing
（阴影效应）
Scattering（散射）
Diffraction
（衍射）
Line-of-sight path {LOS}
Scattering
（散射）
Mobile station
Reflection（反射）
Fading: variation of the received signal power due to the environment, multipaths, and mobility.
Environment
Multipaths
Mobility
Distance between the Tx and Rx
Power
Path Loss, P
Shadowing, S
Multipath Fading, h
Large Scale Fading
Small Scale Fading

## Slide 7: IV. Multipath Fading
Wireless
Channel
Wireless Channel
Transmitter
(Tx)
Receiver
(Rx)
Wireless System
Signal System
  cn: amplitude of the nth propagation path.
  time delay of the nth propagation.
  phase of the nth propagation.
  TV: time-varying
Time-invariant
(Linear TV system)
TV channel impulse response
(system function):

## Slide 8: Channel Impulse Response
Assumption: The distance between the BS and the MS is sufficiently large so that the radio propagation environment can be modeled as two-dimensional (2-D).
Tx
Scatterers
Rx
Fixed Rx:
Rx
c : speed of light
Multipath
Moved Rx:
Maximum Doppler frequency
Motion of the Rx
(multiple antennas)
Multiple antennas

## Slide 9: Duality of Wireless Channels
Time domain,
Frequency domain,
Space domain,
Delay domain,
Angle domain,
Doppler domain,
Duality: to express the same phenomena in different domains.
Fourier Transform
8 system functions
Properly utilize the concept of duality may help understand some puzzles！

## Slide 10: Dispersion and Seclectivity of Wireless Channels
Time domain,
Frequency domain,
Space domain,
Delay domain,
Angle domain,
Doppler domain,
Fourier Transform
Dispersion: spread effect of wireless channels, which means that wireless channels spread the transmitted signal in a certain domain.
Selectivity: wireless channel changes over a certain domain.
Selectivity
Dispersion
Duality

## Slide 11: Delay Dispersion
Tx
Scatterers
Rx
Delay dispersion: multipaths with different time delays lead to the spread of the transmitted signal.
  Measured by delay spread, Des, .
Symbol duration, Ts
Symbol duration
Delay spread
Ts > Des
No inter-symbol interference (ISI)
Narrowband (frequency non-selective) channels
Ts <= Des
Inter-symbol interference (ISI)
Wideband (frequency selective) channels
Symbol duration
Impulse response:

## Slide 12: Frequency Seclectivity
Bs
Frequency selectivity: channel changes over frequency.
  Measured by coherence bandwidth, CB : the bandwidth over which channels express similar characteristic.
Fourier transform
Impulse response
Transfer function
CB
Symbol duration, Ts
Bs < CB
Narrowband (flat fading/frequency non-selective) channels
Bs >= CB
Wideband (frequency selective) channels
CB

## Slide 13: Delay Dispersion-Frequency Selectivy Duality
Transfer function
CB
Fluctuation
CB
Des
Reciprocal
Des
FD
FD
DD
A wireless channel with higher Des (lower CB) is easier to be a wideband channel.
A wireless system with higher transmission rate (higher signal wideband) is easier to incur wideband channels.
FD: frequency domain
DD: Delay domain

## Slide 14: Time Selectivity
Time variant function:
Tx
Scatterers
Rx
Rx
Time selectivity: channel changes over time.
  Measured by coherence time, CT : the time period over which channels express similar characteristic.
CT
Ts < CT
Slow fading channels
Ts >= CT
Fast fading (time-selective) channels
Symbol duration, Ts
Time domain,
Frequency domain,
Space domain,
Delay domain,
Angle domain,
Doppler domain,
Fourier Transform
Selectivity
Dispersion
Duality

## Slide 15: Doppler Dispersion
Tx
Scatterers
Rx
Doppler dispersion: the motion of the Rx results in a broadening of the transmitted signal spectrum.
  Measured by Doppler spread, Ds , .
Doppler spread
Inverse Fourier transform
Bs
Bs > Ds
Slow fading channels
Bs <= Ds
Fast fading (time-selective) channels

## Slide 16: Doppler Dispersion-Time Selectivy Duality
Ds
Time variant function
CT
Fluctuation
Ds
Reciprocal
TD
TD
DD
A wireless channel with higher Ds (lower CT) is easier to be a fast fading channel.
A wireless system with higher transmission rate (higher signal wideband) is easier to incur slow fading channels.
CT
TD: time domain
DD: Doppler domain

## Slide 17: Space Selectivity
Tx
Scatterers
Rx
CS
Space variant function:
Space selectivity: channel changes over locations.
  Measured by coherence distance, CS : the distance over which channels express similar characteristic.
Ss < CS
Spatial correlated channels
Ss >= CS
Spatial uncorrelated channels
Space separation between any two antennas in a multiple antenna array: Ss
Time domain,
Frequency domain,
Space domain,
Delay domain,
Angle domain,
Doppler domain,
Fourier Transform
Selectivity
Dispersion
Duality

## Slide 18: Angle Dispersion
Tx
Scatterers
Angle dispersion: multiple antennas lead to the spread of the transmitted signal in angle domain.
  Measured by angle spread, As , .
Angle dispersion also relates to the pattern of multiple antenna arrays!
angle spread
Inverse Fourier transform

## Slide 19: Angle Dispersion-Distance Selectivy Duality
As
Time variant function
CS
Fluctuation
As
Reciprocal
SD
SD
AD
A wireless channel with higher As (lower CS) is easier to be a spatial uncorrelated channel.
A multiple antenna wireless system with larger antenna spacing is easier to incur spatial uncorrelated channels.
CS
SD: space domain
AD: Angle domain

## Slide 20: V. Main Plot
Fading
Large-scale fading
(cell-cite plan)
Path loss
Shadowing
Small-scale fading
(system design)
8 system functions
Dispersion
Selectivity
Delay dispersion
Doppler dispersion
Angle dispersion
Frequency selectivity
Time selectivity
Space selectivity
Des
Ts
Bs
Ss
CB
Ds
CT
As
CS
Narrowband channel
Wideband channel
Slow fading channel
Fast fading channel
Spatial correlated channel
Spatial uncorrelated channel
Bs
Duality
Duality
Duality
Reciprocal
Reciprocal
Reciprocal
Space domain
Frequency domain
Time domain
Doppler domain
Angle domain
Delay domain
Reciprocal
Reciprocal
Ts
Duality

## Slide 21
Thank you for your attention!